## Slide 1: Weekly Report
Presenter: Kuan-Hsun-Duh
Advisor: Cheng-Wen Wu
2021/07/22

## Slide 2: Outline
Power system
  Zero sequence current
BTB system
  Swiching component
Motor drive system
  Harmonic current effect
Proposed BTB system/Motor drive system
Conclusion & Future Work

## Slide 3: Power System
Three-phase power systems
  conductor currents
   much thinner and lighter wire
Load type:
  3 phase delta & triangular:Motar
  Single phase:House appliance,light……
REF. Paul Evans 2018 2 the Engineering Mindset.com
England Lancaster University

## Slide 4: Zero Sequence Current
Phase currents aren’t equal and displaced not by exactly 120°
Different phase component
  Positive sequence current
  Negative sequence current
    Result in twice flux and rotational velocity
    Eddy currents and heating problem
  Zero sequence current
    n-phase network will sum to n times the magnitude
Figure.1
Ideal 3 phase current

## Slide 5: Back To Back System
Application:
  HVDCT(High Voltage Direct Current Transmission)
Tradictional:
  2 PWM Converter connect together prevent zero sequence current problem
  Cons:Bulky
2 generation:change switching as
  IGCT (Integrated Gate-Commutated Thyristor)
  IEGT(Injection Enhanced Gate Transistor)
    Cons: Zero Sequence Current happened

## Slide 6: Switch Component
Device characteristic | Power bipolar | Power MOSFET | Power MOSFET | IGBT | IGBT | IEGT | GTO | IGCT
Transistor |  |  |  |  |  |  | Thyristor | 
Voltage rating | <1kV | <1 kV |  | >1 kV |  | >4kv | Higher than transistor | 
Gate turn-off thyristor (GTO)
Integrated gate-commutated thyristor(IGCT)
Figure2. IGCT
Frequency:
  Power MOSFET>IGBT(10kHz)
    Automotive electronics
  IGCT(kHz)>GTO(100~800Hz)
P
N
P
P
P
N
N
Notes: IGBT lifetime is ten times greater than IGCT.
3 layer vs 4 layer

## Slide 7: Harmonic current effect
Origin: nonlinear load(diode,transistor……..)
Total Harmonic Distortion (THD)
Reduce method:
  Delta connections control
  3rd harmonic current

## Slide 8: Motor drive system
Pros:
  Reduce harmonic current effect(caused by nonlinear component)
Cons:
  Can’t regernerate power back to the system
REF.A new approach to enhance power quality for medium voltage AC drives
P. W. Hammond Jan.-Feb. 1997 IEEE ASIRobicon USA
Notes: 整流擺放位置導致無法回沖

## Slide 9: Motor drive system result
IEEE Standard 519-1922
REF.A new approach to enhance power quality for medium voltage AC drives
P. W. Hammond Jan.-Feb. 1997 IEEE ASIRobicon USA

## Slide 10: Back To Back System(proposed)
For 6.6kV system
  Single converter ac side is 6600/N
  Cascaded converter produce M-level voltage waveform
    No need switching ripple filter
DC
AC
AC
DC
DC
DC
AC
AC
REF. A Bidirectional Isolated DC–DC Converter as a Core Circuit of the Next-Generation Medium-Voltage Power Conversion System
March 2007
Shigenori Inoue
Tokyo Institute of Technology

## Slide 11: Motor drive system(proposed) Result
Model spec
  Power:10kW
  Votage:350V
  20kHz
Zero voltage switching loss
Conducting loss
REF. A Bidirectional Isolated DC–DC Converter as a Core Circuit of the Next-Generation Medium-Voltage Power Conversion System
March 2007
Shigenori Inoue Tokyo Institute of Technology

## Slide 12: Conclusion & Future Work
Analyze method
  Zero sequence current
  Harmonic current effect
    IEEE Standard 519-1922
LTSPICE environment setup
  (8/12 will have a online lesson)
Design simple circuit(RC circuit)
  REF. Passive Circuit Analysis with Ltspice 2020 11 author:May, Colin Percy University of Westminster

## Slide 13: END

## Slide 15
19 level waveform

## Slide 19
在同一power system 下 掛載三種不同附載