## Slide 1: Weekly Report
Laboratory of Reliable Computing
Department of Electrical Engineering
National Cheng Kung University
指導教授：吳誠文
報告：周昱佑 、 程亞淇、杜冠勳
2021/05/06

## Slide 2: Review

## Slide 3: Controller FSM
WRITE MEM: Transfer data from BRAM to local buffer
READ MEM: Transfer data from local buffer to ASIC
READ RESULT: Transfer result from ASIC to local buffer
WRITE RESULT: Transfer result from local buffer to BRAM

## Slide 4: Controller Architecture

## Slide 5: Problem
In 200MHz /100 MHz
Simulation pass
Synthesis pass
Implementation timing failed.
  Setup time failed
  In 125MHz/100MHz pass
Probable reason: BRAM path too long

## Slide 6: Future Work
Solve timing problem.
Connect to 冠勳’s design.
Learn how to display on LCD.

## Slide 7: Review
FPGA
USB port transfer DATA
OS : Windows
Programming language : C

## Slide 8: Flow Process
open thread
create UART port
open source data file
START
read answer time !=30
read/write flag==1
Yes
No
read answer from FPGA
read source data to buffer
write buffer data to FPGA
free buffer
read/write flag set to 0
read answer time++
※thread process
※main process
count 1 sec
read/write flag set to 1
START
read/write flag set to 1
End
No
Yes
Read answer time==30
End
No
Yes

## Slide 9: Problem
Windows10 does not support “pci-tree”
UART has some problem on setting (sloved)

## Slide 10: Future work
Make API (UART_port C code)
To know WinDriver or PCIScope user guide
暑假實習 -- 逆變器、SiC 功率元件/模組

## Slide 11: UART communication with FPGA
IP List
  MicroBlaze(soft-core processor)
    Architechture can be configurable
    Enable interrupt mode
    Interrupt module cannot have empty connection
  Uart_16550
    Axi_uartlite cannot be used
    Connect the interrupt line to the microblaze
    CP2102 has a max baud rate of 1 Mbps.
Notes: architechture cache size, pipeline depth (3-stage, 5-stage, or 8-stage), embedded peripherals, memory management unit, and bus-interfaces
MicroBlaze's overall throughput is substantially less than a comparable hard CPU core (such as the ARM Cortex-A9 in the Zynq).
32-bit/64-bit

## Slide 12: SDK C code design
Prog Image_filter
  Step1 PC send a photo (bmp format )to FPGA and store data in local cache.
  Step2 microblaze processor do some calculation with pixel value(255-pixel value)
  Step3 FPGA send back the calculated data to PC port and store the data as bmp format.

## Slide 13: SDK C code design
使用 teraterm 傳送資料時 必須選用二進制
使用 日記生成圖片時 必須選用二進制
若程式中迴圈失效 可能是FPGA 設計的memory 不足夠使用導致 迴圈設計失效 FPGA design 的memory 大小可於 Linker Script 文件中查看
Uart 傳輸中若遇到資料遺失 可用兩種方法解決#include “sleep.h” 加入wait 的設計 若上述方法仍無法解決則可依 缺失的資料數補足 dummy data 0x00
#include “xuartns550_i.h”#include “xuartns550.h“ uart driver C code 函式庫
#include <stdlib.h> 記憶體宣告函式庫

## Slide 14: System design flow
1. Image 512*512 bmp format
2. Filter process
(255-pixel value)
3. Send back data to PC
Teraterm is used monitoring COM PORT

## Slide 15: Prog1 Result

## Slide 16: Prog2 Result
Image filter

## Slide 17: Future Work
與昱佑 PC 端 程式互接 傳送圖片或 影像
與亞淇 的control module 互接