## Slide 1: Weekly Report
Presenter: Kuan-Hsun-Duh
Advisor: Cheng-Wen Wu
2021/09/16

## Slide 2: Outline
Power analyzing
  Reactive power loss
TPS Control
  Backflow Power
  Minimum Backflow Power Conrtrol
    Backflow Simulation Result
    GMPBPC v.s GMPSPC in rms current result
  Non-Active Power Transmissions
  Minimum Non-Active Power Transmission Time Control
    Backflow Simulation Result
    Effective Power Transmission Time Ratio Result
    MNPC v.s GMBPC in rms current result
Conclusion
Proposal
REF. Backflow Power Optimization Control for Dual Active Bridge DC-DC Converters
Beijing Jiaotong University Fei Xiong accepted by MDPI in 10 August 2017
Notes: MDPI 5th largest publisher overall in terms of journal paper output.

## Slide 3: Power analyzing
Switch current(Backflow power)
Rms current (reactive component)
Load current
rms current
Switch current

## Slide 4: Power analyzing (Capacitor Loss)
Loss caused by ESR
  Given tan
Loss model
  (relevant to operation freqency)
Time(ms)
(A)
Period
0A

## Slide 5: TPS Control
5 operation mode
  Low power operation
    mode1~mode4
  High power operation
    mode5
REF. Backflow Power Optimization Control for Dual Active Bridge DC-DC Converters
Beijing Jiaotong University Fei Xiong accepted by MDPI in 10 August 2017

## Slide 6: Backflow Power
Primary side
Secondary side
Transmission power flowback
REF. Backflow Power Optimization Control for Dual Active Bridge DC-DC Converters
Beijing Jiaotong University Fei Xiong accepted by MDPI in 10 August 2017

## Slide 7: Minimum Backflow Power Conrtrol
Low power level
  Optimal opject :
  mode1~ mode4
REF. Backflow Power Optimization Control for Dual Active Bridge DC-DC Converters
Beijing Jiaotong University Fei Xiong accepted by MDPI in 10 August 2017
Initial condition :mode 1 constraint :
0,
should satisfy …..(1)
By K= (- +2) (mode1 operation region) & (1)
=>;
: transmission power factor =
: Constant coefficient =
: Transformer phase delay
: Voltage conversion ratio

## Slide 8: Minimum Backflow Power Conrtrol
Boundary point
  =
  =
  =
  = -
REF. A Study on Modulation Strategies of Dual Active Bridge DC–DC Converter for Battery Energy Storage Systems Ritsumeikan University March 2019
Author :Muhammad Hazarul Azmeer bin Ab Malek
Notes: ResearchGate針對科學專家學者提供一個研究分享平台。研究人員可以以註冊該網站而免費的分享全球各個領域尖端科學專家學者最新科研成果和學術著作，而且能夠按照他們的意願迅速擴大整個研究領域對自己的研究成果的關注。

## Slide 9: Minimum Backflow Power Conrtrol
By ZCS condition
  =
  ≥ 0
  0
REF. A Study on Modulation Strategies of Dual Active Bridge DC–DC Converter for Battery Energy Storage Systems Ritsumeikan University March 2019
Author :Muhammad Hazarul Azmeer bin Ab Malek
Notes: ResearchGate針對科學專家學者提供一個研究分享平台。研究人員可以以註冊該網站而免費的分享全球各個領域尖端科學專家學者最新科研成果和學術著作，而且能夠按照他們的意願迅速擴大整個研究領域對自己的研究成果的關注。

## Slide 10: Minimum Backflow Power Conrtrol
Mode 4 has maximum k value
widest power range for zero backflow power
REF. Backflow Power Optimization Control for Dual Active Bridge DC-DC Converters
Beijing Jiaotong University Fei Xiong accepted by MDPI in 10 August 2017
By transmission power k=
; )
=>d(1-d) when

## Slide 11: Minimum Backflow Power Conrtrol
High Power Level
  Operation in mode 5
    GMPBPC
    GMSBPC
High Power Level
  GMBPC
REF. Backflow Power Optimization Control for Dual Active Bridge DC-DC Converters
Beijing Jiaotong University Fei Xiong accepted by MDPI in 10 August 2017

## Slide 12: Backflow Simulation Result
At lower power level reduce backflow power effectively
GMPBPC has worse optimized results than GMSBPC when d >1
d>1(boost)
(w)
(w)
(w)
d<1(buck)

## Slide 13: GMPBPC v.s GMPSPC in rms current result
GMPBPC has worse optimized results than GMSBPC when d >1 in high voltage transmission
  Larger conduction losses arise
boost
buck

## Slide 14: Non-Active Power Transmission
Backflow power non-Active Power
Primary side
Zero power
Positive power(maximum power transmission effciency)
backflow power
: primary non-active power time
: primary equivalent zero power time
primary zero power time
effective power transmission time

## Slide 15: Non-Active Power Transmission
non-active power transmission time ratio (NTR)
  =
effective power transmission time ratio primary side (ETR)
effective power transmission time ratio
REF. Backflow Power Optimization Control for Dual Active Bridge DC-DC Converters
Beijing Jiaotong University Fei Xiong accepted by MDPI in 10 August 2017

## Slide 16: Minimum Non-Active Power Transmission Time Control(MNPC)
Object : Maximize or Minimize
GMBPC
MNPC
REF. Backflow Power Optimization Control for Dual Active Bridge DC-DC Converters
Beijing Jiaotong University Fei Xiong accepted by MDPI in 10 August 2017

## Slide 17: Backflow power comparison
MNPC and GMBPC is much smaller than the backflow power of SPS control especially at lower power level.
REF. Backflow Power Optimization Control for Dual Active Bridge DC-DC Converters
Beijing Jiaotong University Fei Xiong accepted by MDPI in 10 August 2017

## Slide 18: Effective Power Transmission Time Ratio Result
MNPC has a better performance than GMBPC on the reduction of non-active power transmission
in GMBPC is even smaller than in SPS control when d approach to 1
60V  120V
80V  120V
REF. Backflow Power Optimization Control for Dual Active Bridge DC-DC Converters
Beijing Jiaotong University Fei Xiong accepted by MDPI in 10 August 2017

## Slide 19: MNPC v.s GMBPC in rms Current
The current rms of GMBPC are even larger than that of SPS control whn d approach to 1
60V  120V
80V  120V
REF. Backflow Power Optimization Control for Dual Active Bridge DC-DC Converters
Beijing Jiaotong University Fei Xiong accepted by MDPI in 10 August 2017

## Slide 20: Implementation
Experiment flow

## Slide 21: Implementation result
REF. Backflow Power Optimization Control for Dual Active Bridge DC-DC Converters
Beijing Jiaotong University Fei Xiong accepted by MDPI in 10 August 2017
d>1(boost)
d<1(buck)

## Slide 22: Conclusions
MNPC achieves both the maximum effective power transmission time and minimum current stress
GMBPC and MNPC are two effective methods when d is far from 1
in GMBPC decreases when approaches to 1 while in MNPC and SPS increases when d approaches to 1.
A prototype is built to verify the effectiveness of theoretical analysis and the proposed control methods

## Slide 23: Proposal
Build a simulation tool
  Find the best optimization method under specific constraint
Future work
  Algorithm
  Power calculation model
  Scripting ltspice
  Sql database control

## Slide 24: Backflow Control Parameter
D1 : Primary side inner phase delay
(Q1 v.s Q3)
D2 : Secondary side inner phase delay
(Q5 v.s Q8)
: Transformer phase delay
GMPBPC
GMSBPC
GMBPC