## Slide 1: Weekly Report
Presenter: Kuan-Hsun-Duh
Advisor: Cheng-Wen Wu
2021/10/05

## Slide 2: Outline
Recap
  Backflow power
  Proposal
IBDC_DAB with PI control
  SPS control without Algorithom(matlab)
  Proposed method
Expectation effect and problem
Future work

## Slide 3: Control method
Voltage mode control
Peak current control method
電流控制模式
  斜率補償技術(比較器之所以會有鋸齒波的存在)
  因為duty超過50% 容易產生震盪()

## Slide 4: 回授穩定度分析
前述的兩種控制 又可細分DCM CCM design
DCM 通常會加入CT module 來調控電流
電壓控制模式
  降壓模式中 以 CCM 為最常見設計
Phase margin 代表電路穩定度 反應變化的能力
系統若有一極點在右半平面則會不穩定

## Slide 5: 回授補償電路
3種type
單極點
  低頻有高阻抗 但交越頻率低於諧振頻率 造成暫態響應極差
極零點配對
  DC 射極點 後有1 zero 在增益維持住
雙極點 雙零點
  離的越開 phase margin 則會越大
  雙 zero 用於抵消 輸出濾波器的極點特性
  極點用於 抵銷電容產生的 zero
  另外的極點用於 在高頻時確保其增益不會下降

## Slide 6: 控制器比較
數位控制器
  優勢: 可調節 便宜 抗雜訊能力好
  弱勢:

## Slide 7: Backflow Power(Recap)
Primary side
Secondary side
Transmission power flowback
REF. Backflow Power Optimization Control for Dual Active Bridge DC-DC Converters
Beijing Jiaotong University Fei Xiong accepted by MDPI in 10 August 2017

## Slide 8: Proposal(Recap)
Build a simulation tool
  Find the best optimization method under specific constraint
Future work
  Algorithm
  Power calculation model
  Scripting ltspice
  Sql database control

## Slide 9: IBDC_DAB with PI control
IBDC_DAB by PI control in SPS way
Switching tunable
  Silmiler to ltspice simulation result

## Slide 10: SPS control without Algorithom
Delay parameter
System output voltage
Error
Goal value

## Slide 11: Problem analysis
Goal:
  Help system to tune the duty-cycle to achieve the goal value(backflow value) more quickly
Method:
  Add machine learning block after PI control block
Fig2. Proposed architecture
Fig1. Traditional architecture

## Slide 12: Proposed method
Initial condition: first set point by algorithom
  Yellow path weight iniatilize to 1
  Other weight iniatilize to 0

## Slide 13: Expectation effect and problem
Problem1:
  Condition:
    optimized duty cycle(after ML training) don’t have the big difference compare with initial duty cycle(mathmetical model )
    The optimized duty cycle is 30%(after ML training)
    Switching Initial start from 25% (mathmetical model )
Problem2:
  Condition :
    optimized duty cycle(after ML training) don’t have the big difference compare with initial duty cycle(mathmetical model )
    optimized duty cycle is 24% Initial start from 25%

## Slide 14: Future work
How to tuning PID control parameter
  :
    Make the output value closed to the goal value
  :
    Control the steady state error
  :
    Adjust variation slope prevent the output value oscillating
PI is more often used in power supply

## Slide 15: Future work
PID controller + Algorithom & design (TPS control)
Algorithom implement by the reference paper
REF. Backflow Power Optimization Control for Dual Active Bridge DC-DC Converters
Beijing Jiaotong University Fei Xiong accepted by MDPI in 10 August 2017

## Slide 16: Future work
Proposal problem should be redefined
  Keep study on electric vehicle issue
SNN training software implementation
  STBP
  STDP
  TSSL-BP