## Slide 1: Weekly Report
Presenter: Kuan-Hsun-Duh
Advisor: Cheng-Wen Wu
2021/10/12

## Slide 2: Outline
Recap
  Backflow power
  Original control flow
Proposal
  Problem analysis
  Proposed control flow
Expectation effect and problem
  Replacing PID with machine learning method

## Slide 3: Outline
Controller design
  PID parameter
  Control method
  Feedback Stability
  Compensation circuit
Experiment build up
  SPS control without Algorithom(matlab)
Future work

## Slide 4: Backflow Power(Recap)
Primary side
Secondary side
Transmission power flowback
REF. Backflow Power Optimization Control for Dual Active Bridge DC-DC Converters
Beijing Jiaotong University Fei Xiong accepted by MDPI in 10 August 2017

## Slide 5: Original control flow
PI controller + Algorithom & design (TPS control)
Algorithom implement by the reference paper
REF. Backflow Power Optimization Control for Dual Active Bridge DC-DC Converters
Beijing Jiaotong University Fei Xiong accepted by MDPI in 10 August 2017

## Slide 6: Problem analysis
Goal:
  Help system to tune the duty-cycle to achieve the goal value(backflow value) more quickly with time
Method:
  Add machine learning block after PI control block
Fig2. Proposed architecture
Fig1. Traditional architecture

## Slide 7: Proposed control flow
Initial condition: first set point by algorithom
  Yellow path weight iniatilize to 1
  Other weight iniatilize to 0

## Slide 8: Expectation effect and problem
Expectation effect
  transition (low load to high load) reaction time will be improved with time.
Problem
  Control is not an NP problem
  Controller can be tunable by human

## Slide 9: Deep learning replacing PID
REF. On Replacing PID Controller with Deep Learning Controller for DC Motor System
Kangbeom Cheon, Kyungpook National University,Korea, December, 2015.

## Slide 10: Step response Result
Rise time : deep learning < PID control
Overshoot : deep learning > PID control

## Slide 11: Result
Residuals : the variance of error
RMSE:root-mean-square deviation

## Slide 12: Result

## Slide 13: PID parameter
How to tuning PID control parameter
  :
    Make the output value closed to the goal value
  :
    Control the steady state error
  :
    Adjust variation slope prevent the output value oscillating
PI is more often used in power supply

## Slide 14: Control method
Voltage mode control
Peak current control
Other control method
  Vally current control method
  Emulated current mode control
  Hysteretic current mode control
  Average current mode control

## Slide 15: Voltage mode control
REF.切換式電源轉換器-吳義利

## Slide 16: Peak current control method
Pros : Obtain inactive current from switching
Cons : Switching duty cycle >50 % will cause current osicallating
Red line : + +
duty cycle > 50 %
Black line : +
duty cycle = 0
Red line : +
duty cycle > 50 %
Black line : +
duty cycle = 0
REF.切換式電源轉換器-吳義利
Notes: 限流保護電路作用
較快的反應速度

## Slide 17: Feedback Stability
Small signal analyze
  Step1 : calculate the transfer function on block1 : & block2
  = *
  Step2 : design the error amplifier
1
2
3

## Slide 18: Feedback Stability (Peak current control method)
Reducing inactive current by current transformer module
REF.切換式電源轉換器-吳義利

## Slide 19: Compensation circuit
Single Pole Amplifier(integrator circuit)
  High resistance in low frequency
  =>bad transient response
Zero Pole Pair Amplifier
  Pole set at DC point , the gain will be constant
  between
REF.切換式電源轉換器-吳義利
Notes: 高阻抗 輸出電壓大

## Slide 20: Compensation circuit
Two Pole two zero Amplifier (Circuit with L-C filter)
  Distance brtween phase margin
  is used to eliminate the pole of the output filter
  is used to eliminate the zero produced
  by the ESR of the capacitor
  is used to maintain the gain at high frequency
REF.切換式電源轉換器-吳義利

## Slide 21: Controller design (phase margin)
Phase margin should >
Transfer function :
  =0 unstable
& phase margin trade off
  transient response time phase margin

## Slide 23: Compensation circuit
Circuit | Control | Operation region | Compensation circuit
Buck converter Forward converter Full-bridge converter | Voltage mode control | DCM | 
 |  | CCM | Type1 , Type2
 | Peak current control | DCM | 
 |  | CCM | Type3 , Type2
Flyback converter Buck–boost converter Boost converter | Voltage mode control | DCM | Type1 , Type2
 |  | CCM | Type1 , Type2
 | Peak current control | DCM | Type1 , Type3
 |  | CCM | Type1 , Type2
REF.切換式電源轉換器-吳義利
Notes: 降壓-升壓變換器和返馳式變換器等效

## Slide 24: IBDC_DAB with PI control
IBDC_DAB by PI control in SPS way
Switching tunable
  Silmiler to ltspice simulation result

## Slide 25: SPS control without Algorithom
Delay parameter
System output voltage
Error
Goal value

## Slide 26: Future work
Proposal problem should be redefined
  Discrete control design
SNN training software implementation
  STDP(2015)
  STBP(2018)
  TSSL-BP(2020)

## Slide 27: End
Thank you for listening

## Slide 28: Traditional control architecture
Algorithom
  MNPC(Minimum Non-Active Power Transmission Time Control)
  GMBPC (Global Minimum Backflow Power Control)
REF. Backflow Power Optimization Control for Dual Active Bridge DC-DC Converters
Beijing Jiaotong University Fei Xiong accepted by MDPI in 10 August 2017

## Slide 29: Expectation effect and problem
Problem1:
  Condition:
    optimized duty cycle(after ML training) don’t have the big difference compare with initial duty cycle(mathmetical model )
    The optimized duty cycle is 30%(after ML training)
    Switching Initial start from 25% (mathmetical model )
Problem2:
  Condition :
    optimized duty cycle(after ML training) don’t have the big difference compare with initial duty cycle(mathmetical model )
    optimized duty cycle is 24% Initial start from 25%

## Slide 30: Feedback Stability (Voltage mode control)
Buck converter usually operate in CCM mode
  The transfer function) output is related to input voltage
REF.切換式電源轉換器-吳義利
Notes: 須負載低於一定的值 才會操作在DCM