## Slide 1: Weekly Report
Presenter: Kuan-Hsun-Duh
Advisor: Cheng-Wen Wu
2021/10/26

## Slide 2: Outline
Background
  Architecture
  Switching Component
  Driving Circuit
Control Background
  Backflow Power
Conclusion

## Slide 3: Outline
Background
  Architecture
  Switching Component
  Driving Circuit
Control Background
  Backflow Power
Conclusion

## Slide 4: Background
Application : charging circuit
PFC : power factor circuit

## Slide 5: Architecture (Prof. Pai)
Full bridge converter with center‑tapped transformer
REF. 切換式電源轉換器 吳義利編著

## Slide 6: Architecture (Research)
A Study on Switching component of Dual Active Bridge DC-DC Converter for Battery Storage system

## Slide 7: Switching Component
Background : SiC with high operating frequency with low conduction loss compared with IGBT & mosfet
Chart: 
| 75khz | 150khz | 250khz
諧振電感(uH) | 1100 | 482 | 281
諧振電容(nf) | 4.7 | 2.5 | 1.5
Chart: 
| 75khz | 150khz | 250khz
電桿鐵蕊(mm^3) | 117485.55 | 50530 | 20258.46
變壓器鐵蕊(mm^3) | 13442.1 | 9596.16 | 9129.12
Notes:   SiC 300kHz 但頻率太高也不是說很建議
  目前設計規格落在150K
  IGBT < 100kHz for charging system
  Mosfet 100kHz for charging system
    Cool mosfet 規格可更高
  驅動器電路 20-30 kHz
  PFC system <100kHz 但高電壓
  GAN 500kHz Apple 手機 低電壓
  頻率越高 可以降低 感性的元件的設計 以及transformer 的設計大小
  頻率越高也可以抑制 輸出的電壓連波
  SiC ≅ 300kHz 但頻率太高也不是說很建議
  目前設計規格落在150K
  IGBT < 100kHz for charging system
  Mosfet ≅ 100kHz for charging system
    Cool mosfet 規格可更高
  驅動器電路 ≅ 20-30 kHz
  PFC system <100kHz 但高電壓
  GAN ≅ 500kHz Apple 手機 低電壓
  頻率越高 可以降低 感性的元件的設計 以及transformer 的設計大小
  頻率越高也可以抑制 輸出的電壓連波

## Slide 8: Driving Circuit
Figure 1.
光耦合驅動 電光電
Figure 2.
自舉式隔離電路
Figure 3.
Figure 4.工作原理
R1 限制電流大小
RG 控制驅動速度

## Slide 9: Driving Circuit Problem
is high is power mosfet
Turn-off make Cgd induce huge current flow to Cgs Vgs Circuit shorted (red line & blue line)

## Slide 10: Driving Circuit Solution
Increase Cgs
Active Miller Clamp

## Slide 11: Outline
Background
  Architecture
  Switching Component
  Driving Circuit
Control Background
  Backflow Power
Conclusion

## Slide 12: Control Background
Digital Control is less susceptible environmental variations , less sensitive to noise, easily adjusting
  FPGA , Microcontroller unit
Sample freq > 10 freq

## Slide 13: Backflow Power
Primary side
Secondary side
Transmission power flowback
REF. Backflow Power Optimization Control for Dual Active Bridge DC-DC Converters
Beijing Jiaotong University Fei Xiong accepted by MDPI in 10 August 2017
D1 : Primary side inner phase delay
(Q1 v.s Q3)
D2 : Secondary side inner phase delay
(Q5 v.s Q7)
: Transformer phase delay

## Slide 14: Implementation
Experiment flow
REF. Backflow Power Optimization Control for Dual Active Bridge DC-DC Converters
Beijing Jiaotong University Fei Xiong accepted by MDPI in 10 August 2017

## Slide 15: Experiment
Environment :
  Matlab Simulink
  Matlab Simscape library
REF. Backflow Power Optimization Control for Dual Active Bridge DC-DC Converters
Beijing Jiaotong University Fei Xiong accepted by MDPI in 10 August 2017

## Slide 16: Outline
Background
  Architecture
  Switching Component
  Driving Circuit
Control Background
  Backflow Power
Conclusion

## Slide 17: Conclusion
Future Work
  Analyze different component (SiC Mosfet GaN......)operate at different frequency in DAB_IBDC
  Experiment on LTSPICE & PSIM & Q3D
  Experiment on Matlab for discrete control system