## Slide 1: Weekly Report
Presenter: Kuan-Hsun-Duh
Advisor: Cheng-Wen Wu
2021/04/01

## Slide 2: UART communication with FPGA
IP List
  MicroBlaze(soft-core processor)
    Architechture can be configurable
    Enable interrupt mode
    Interrupt module cannot have empty connection
  Uart_16550
    Axi_uartlite cannot be used
    Connect the interrupt line to the microblaze
    CP2102 has a max baud rate of 1 Mbps.
Notes: architechture cache size, pipeline depth (3-stage, 5-stage, or 8-stage), embedded peripherals, memory management unit, and bus-interfaces
MicroBlaze's overall throughput is substantially less than a comparable hard CPU core (such as the ARM Cortex-A9 in the Zynq).
32-bit/64-bit

## Slide 3: SDK C code design
Environment:Vitis Software Platform
Prog1 FPGA Send Message To UART
  The microblaze send message by byte to PC port and display the result in terminal
  Library : xil_printf.h
  Src資料夾右鍵>New>other>C/C++
  >Source file(新增C code file)
Xil_printf 函式

## Slide 4: SDK C code design
Prog2 Image_filter
  Step1 PC send a photo (bmp format )to FPGA and store data in local cache.
  Step2 microblaze processor do some calculation with pixel value(255-pixel value)
  Step3 FPGA send back the calculated data to PC port and store the data as bmp format.

## Slide 5: SDK C code design
使用 teraterm 傳送資料時 必須選用二進制
使用 日記生成圖片時 必須選用二進制
若程式中迴圈失效 可能是FPGA 設計的memory 不足夠使用導致 迴圈設計失效 FPGA design 的memory 大小可於 Linker Script 文件中查看
Uart 傳輸中若遇到資料遺失 可用兩種方法解決#include “sleep.h” 加入wait 的設計 若上述方法仍無法解決則可依 缺失的資料數補足 dummy data 0x00
#include “xuartns550_i.h”#include “xuartns550.h“ uart driver C code 函式庫
#include <stdlib.h> 記憶體宣告函式庫

## Slide 6: System design flow
1. Image 512*512 bmp format
2. Filter process
(255-pixel value)
3. Send back data to PC
Teraterm is used monitoring COM PORT

## Slide 7: Prog1 Result

## Slide 8: Prog2 Result
Image filter

## Slide 9: Future Work
與昱佑 PC 端 程式互接 傳送圖片或 影像
與亞淇 的control module 互接

## Slide 10: Missing image data
補足DATA

## Slide 11: Block diagram

## Slide 12: SRAM
set_property CLOCK_DEDICATED_ROUTE BACKBONE [get_nets design_1_i/clk_wiz_1/inst/clk_in1_design_1_clk_wiz_1_0]
Clock port 針對不同頻率 設計出不同的port 相接

## Slide 13: system clock design

## Slide 14: Block mem default

## Slide 15: Block mem default

## Slide 16: Block mem default

## Slide 17: Block mem default

## Slide 18: XSA file update in IDE

## Slide 19: Mem size adjustment
Click HDL Wrapper will update design
KB
8K==0x2000(byte mem address)

## Slide 20: MEM ckeck
8K= =4(1word 4 byte)=>

## Slide 21: XSA file update in IDE

## Slide 22: IDE mem adjustment

## Slide 23: BMP file format
是從0開始計數 故要+1

## Slide 24: BMP file format

## Slide 25: BMP file format header file
REAL IMG

## Slide 26: Baud rate vs clk frequency

## Slide 27: License
點擊上面欄位 License manager

## Slide 28: Memory Debug
Windows>>show view >> debug
Windows>>show view >> Memory

## Slide 29: Memory debug
Microblaze
ADD ADDRESS monitor
REFRESH
<HSB LSB>

## Slide 30: Compile with Vitis IDE
右鍵>build project
Run as >> 第二個

## Slide 31: Notepad
若mobaxterm 連上 不能編輯 通常因為 bash 檔 有寫指令